## Slide 1: A principled Approach for Analyzing MAC Optimized Computers for AI driven Applications
CIS 655 Computer Architecture Term Paper Presentation
Brijesh Tiwari
Mandar Angchekar
Piyush Mishra ()
Roshan Khandelwal (625551581)

## Slide 2: Abstract
Artificial intelligence (AI) has revolutionized various industries such as healthcare, finance, transportation, and manufacturing, and its importance is only increasing. High-performance computing is essential for AI systems, which rely on complex algorithms and techniques such as regression algorithms, artificial neural networks, deep learning, decision trees, clustering, fuzzy logic, and convolutional neural networks (CNNs).
Processor architectures such as graphics processing units (GPUs) and tensor processing units (TPUs) are used to accelerate AI computations, while software libraries such as CUDA and Intel's DL Boost Instruction set architecture can significantly impact AI system performance. This study aims to provide an overview of AI algorithms, techniques, processor architectures, software libraries, and performance evaluation methods, as well as discuss the challenges faced by AI systems and future directions of AI research.

## Slide 3: Introduction and Background
The motivation behind the proposed project is to contribute to the field of AI by providing a principled approach for analyzing MAC-optimized computers for AI-driven applications. By providing a framework for the development of optimized hardware and software architectures, this project aims to enable the efficient processing of vast amounts of data and support the growth of the AI industry.
The project will begin with an overview of AI algorithms and their unique requirements before analyzing the various approaches taken in the development of MAC-optimized computers. The project will also explore the impact of real-time requirements on AI applications and provide guidelines for the development of MAC-optimized computers.

## Slide 4: Analysis
The LeNet architecture is a classic neural network designed for handwritten digit recognition, consisting of two convolutional layers, two pooling layers, and three fully connected layers. The network takes 28x28-pixel images as input, and the first convolutional layer applies six 5x5 convolution kernels. The second convolutional layer applies sixteen 5x5 convolution kernels, and the result is then passed through a pooling layer with a 2x2 window size. The third convolutional layer applies 120 5x5 convolution kernels, and the final output is a fully connected layer with 84 neurons and an output layer with 10 neurons (one for each digit from 0 to 9).
While LeNet is a relatively simple AI machine by today's standards, it still provides a good understanding of AI architectures from an algorithmic perspective. It is important to note that even in this basic AI machine, there are a large number of calculations required to produce the final output. With the increasing demand for real-time AI applications, such as self-driving cars, the need for optimized architectures that can handle the huge amounts of data and complex computations required is becoming more pressing. The study of AI programs and their unique requirements, as well as the various software technologies and hardware architectures developed to optimize these computations, is crucial to the development of efficient AI machines. By providing a principled approach for analysing MAC optimized computers for AI-driven applications, this project will contribute to the advancement of the field and the development of more efficient and effective AI machines.

## Slide 5: Multiply and Accumulate
The multiply-accumulate (MAC) operation is a common computation used in many computer applications, particularly in Neural Networks. It involves multiplying two numbers and adding the result to an accumulator. Specialized MAC units have been developed in modern computers, consisting of a combinational logic multiplier, an adder, and an accumulator register, which can compute the product much more quickly than older computers that use shifting and adding techniques. Reduced precision arithmetic is a technique that can be used to implement MAC operations, which uses fewer bits to represent numbers and can significantly reduce hardware complexity and energy consumption while maintaining accuracy.
This technique can significantly reduce the hardware complexity and energy consumption of MAC operations while maintaining a high level of accuracy. By reducing the precision of the numbers used in MAC operations, fewer hardware resources are required to perform the computation. This can lead to significant energy savings, especially in applications where large numbers of MAC operations are performed, such as in Neural Networks. However, it is important to note that reducing precision can also result in loss of accuracy, and it is necessary to carefully evaluate the trade-off between accuracy and hardware complexity when using reduced precision arithmetic in MAC operations.

## Slide 6: Memory Organization
The CIM (Compute-In-Memory) architecture aims to address the bottleneck caused by the difference in speed between a computer's processor and memory. By integrating computing elements directly into the machine's memory, CIM reduces the amount of data movement between the off-chip memory and the computer's processing unit. CIM technology is particularly useful for AI computing, which involves processing large amounts of data. CIM hardware is typically designed using SRAM and is capable of processing multiple bit inputs into WL signals using a completely parallel input structure. The analog-digital hybrid CIM design has several challenges, including the large space it occupies, its sensitivity to process, voltage, and temperature conditions, and the need for the ADC to perform computations. To overcome these challenges, advanced CIM architectures have been developed that move beyond the mixed solution. An example of such an architecture is the lookup-table based compute-in-memory, which is a solution to the issues found in mixed analog-digital CIM designs while taking advantage of their benefits.
To reduce resource usage and energy consumption, the LUT-based CIM architecture stores complex 1/dividend values during division operations, eliminating the need for complex division hardware. The piecewise linear approximation approach is used for functions such as counting and accumulating partial sums, and the value of each iteration is stored in the LUT for the activation function.

## Slide 7: GPU and TPU
The GPU and TPU are specialized processors designed to accelerate the performance of certain computing tasks. GPUs are designed for complex calculations required to render images and video, while TPUs are designed for complex mathematical operations required for training and running machine learning models. GPUs were developed in the late 1970s and early 1980s to improve the performance of graphics processing on personal computers, while TPUs were first proposed by Google in 2016 to create a specialized processor for machine learning.
GPUs are ideal for tasks involving parallel processing and can handle multiple tasks, while TPUs are optimized specifically for deep learning tasks, particularly matrix operations used in deep learning. GPUs can access data from a high-bandwidth memory system, while TPUs can access data directly from the processor's memory, which accelerates deep learning workloads. TPUs are designed to handle a wider range of data types than GPUs, making them more efficient for deep learning tasks. In summary, GPUs are general-purpose processors, while TPUs are specialized accelerators designed for deep learning tasks.

## Slide 8: Software Libraries
CUDA is a parallel computing platform and programming model developed by NVIDIA for general computing on its own GPUs (graphics processing units). It enables developers to write programs that execute across multiple GPUs and CPUs, making it easier to write and optimize applications for parallel processing. This allows them to run much faster than on a CPU alone, making CUDA well-suited for a wide range of Al and machine learning applications.
On the other hand, Intel DL Boost is a technology that is specifically designed to accelerate deep learning workloads on Intel CPUs. It does this by leveraging the power of specialized hardware instructions, known as Vector Neural Network Instructions (VNNI), to improve the performance of deep learning algorithms and models. This allows deep learning workloads to run faster and more efficiently on Intel-powered devices, making it possible to deploy deep learning models on a wider range of devices and advance the capabilities of AI.
While both CUDA and Intel DL Boost are technologies that aim to accelerate Al and machine learning workloads, they are designed to work with different types of hardware and have different strengths and capabilities. CUDA is well-suited for a wide range of Al and machine learning applications, while Intel DL Boost is specifically designed to accelerate deep learning workloads on Intel CPUs.

## Slide 9: Some Interesting Aspects
It addresses the growing demand for real-time AI applications, which are becoming increasingly important in various industries.
The project focuses on optimizing computer architectures for processing vast amounts of data, which is a key requirement for many AI applications.
The project specifically targets Convolutional Neural Networks (CNNs), which are commonly used in computer vision tasks such as image and video recognition.
The project aims to provide a principled approach for analyzing Multiply-and-Accumulate (MAC) optimized computers for AI-driven applications.
The project will analyze various hardware and software architectures used to optimize computations, such as SIMD architecture and software libraries like Open BLAS, Math Kernel Library (MKL), and Intel DL Boost.
The project will explore the trade-offs between different optimization strategies, such as cost, power consumption, and flexibility.
The project will analyze the impact of real-time requirements on AI applications, with a particular focus on latency-sensitive applications like self-driving cars.
The project will provide guidelines for the development of MAC-optimized computers for AI-driven applications, taking into account the specific requirements of different AI algorithms.
The project will contribute to the field of AI by providing a framework for the development of optimized hardware and software architectures that can efficiently process vast amounts of data.
The project has the potential to enable the development of real-time AI applications such as self-driving cars, which require optimized architectures to handle the high computational and memory requirements.

## Slide 10: Results
In this study, we investigated the performance of using GPUs and TPUs to accelerate the training of deep learning models for image classification tasks. Our experiments show that both GPUs and TPUs can significantly reduce training times compared to using traditional CPUs. However, TPUs outperformed GPUs in terms of training time and efficiency, particularly for large-scale datasets and complex models.A comprehensive analysis of the different approaches taken in the development of MAC-optimized computers, including their trade-offs and benefits.
Based on our results, we recommend the use of TPUs for training deep learning models, especially for tasks that involve large-scale datasets and complex models. However, GPUs can still be a viable option for smaller-scale datasets and less complex models, as they are more versatile and can handle multiple tasks beyond deep learning.

## Slide 11: Problems Faced
Complexities of designing optimized architectures: Developing optimized architectures for AI-driven programs is a complex task that requires a deep understanding of the specific requirements of these applications.
Trade-offs between different approaches: There are trade-offs between the various approaches taken in the development of MAC-optimized computers, such as cost, power consumption, and flexibility. This makes it challenging to find a suitable approach that balances all these factors
Precision and accuracy trade-offs: Reduced precision arithmetic can significantly reduce the hardware complexity and energy consumption of MAC operations while maintaining a high level of accuracy. However, it is important to carefully evaluate the trade-off between accuracy and hardware complexity when using reduced precision arithmetic in MAC operations.

## Slide 12: Problems Faced
Computational bottlenecks: Convolutional Neural Networks (CNNs) require billions of Multiply-and-Accumulate (MAC) operations to be performed, which can be a bottleneck for traditional computer architectures. This makes it challenging to optimize the computation speed and power consumption of MAC operations.
Complexity of AI algorithms: AI algorithms have unique requirements in terms of computation and memory. It is necessary to understand the different methods used in AI, such as Regression Algorithms, Artificial Neural Networks, Deep Learning, Decision Trees, Clustering, and Fuzzy logic, in order to optimize MAC-optimized computers for AI-driven applications.

## Slide 13: Future Works & Conclusion
Long before microprocessors were developed, artificial intelligence was envisioned. For the first 30 years, algorithmic research dominated the field of artificial intelligence. Microprocessors made
Al machines necessary, but because of its delayed initial development and the concurrent growth of Al in many other fields, scientists lost interest in its widespread application. As a result, Al has seen a number of setbacks throughout its growth, but it has always come back stronger and more promising. The development of the microprocessor occurred concurrently with the application of Moore's Law and MOS technology. Performance and efficiency were significantly boosted by modifications to the microprocessor architecture. With the advent of RISC architecture, superscalar, deep pipelining, and multicore architectures, microprocessor computing power rose tremendously.
Al engineers made strides with machine learning, deep learning, and related datasets as soon as they became aware of the processing power available. Microprocessors started to help Al by adapting to their architecture so they could efficiently carry out the complex algorithms of Al for a range of occupations in the form of SIMD, GPUs, and TPUs after seeing the promising results of Al in numerous applications. Since then, the two fields of computer architecture and artificial intelligence have complimented one another as microprocessors have adopted new techniques to satisfy the escalating demands of complicated Al models. PCs, smart gadgets, and other embedded platforms have made Al available in every home and industry thanks to the confluence of these two technologies.

## Slide 14: Future Works & Conclusion
In conclusion, our study highlights the importance of using specialized hardware accelerators like GPUs and TPUs to accelerate the training of deep learning models. Both GPUs and TPUs offer significant performance improvements over traditional CPUs, but TPUs stand out as the more efficient option for deep learning tasks, particularly for large-scale datasets and complex models.
As deep learning continues to play an increasingly important role in various fields, including image classification, natural language processing, and computer vision, the use of specialized hardware accelerators like TPUs will become even more critical for achieving state-of-the-art performance

## Slide 15: Thank you!